## Slide 1
DIGITAL IMAGE PROCESSING
Digital Image
Acquisition Pipeline
From physical scene to digital data — the stages, key terms,
and where errors enter along the way
Q.27 — Explanation with flowchart

## Slide 2
The Acquisition Pipeline
Five sequential stages convert a real-world scene into a digital image
1
Scene &
Illumination
2
Optics
(Lens)
3
Sensor
(CCD / CMOS)
4
Sampling &
Quantization
5
Digital Image
(Storage)
Photons → Optical image → Electrical signal → Discrete samples → Digital pixel array
Pipeline in one line: Illumination → Optics → Sensor → Sampling → Quantization → Digital Image

## Slide 3
Key Terms at Each Stage
The essential keyword to remember for every stage of acquisition
Illumination
Light source + object reflectance shape the raw scene radiance
Optics / Focusing
Lens forms an optical image; aperture controls light & depth of field
Sensing (Transduction)
CCD/CMOS array converts photons into an analog electrical signal
Sampling
Continuous image is discretized on a spatial pixel grid
Quantization
Each sample's amplitude is mapped to a finite digital gray/color level (bit depth)

## Slide 4
Common Sources of Error
Every stage of the pipeline can introduce a distinct type of image degradation
ILLUMINATION
Uneven lighting
Shadows, glare & low light reduce contrast and raise noise
OPTICS
Lens aberration & blur
Distortion, chromatic aberration, defocus, diffraction limit
SENSOR
Sensor noise
Shot noise, dark current, fixed-pattern noise, blooming
SAMPLING
Aliasing
Undersampling below the Nyquist rate creates moiré artifacts
QUANTIZATION
Quantization error
Limited bit depth causes banding / posterization
Errors compound stage-to-stage — calibration & filtering at each step keep the final image usable.

## Slide 5
Key Takeaways
Pipeline order: Illumination → Optics → Sensor → Sampling → Quantization → Digital Image
Two discretizations: Sampling (space) and Quantization (amplitude) both convert continuous data into discrete digital form
Error accumulates: Noise and distortion from every stage carry forward; fix them as early in the chain as possible
Output: A calibrated digital image — an M×N matrix of quantized pixel values, ready for processing